## Slide 1: Tagore Half-Bridge (HB) GaN EVB:
Tagore Technology
12 May 2022

## Slide 2: Tagore GaN Half-Bridge EVB Overview – GaN HB Daughter Card
Isolated Half-Bridge using Tagore’s 650V GaN FETs with integrated driver IC TP44x00NM.
Isolated Gate drivers for both high-side and low side device.
+5V/0V PWM inputs.
Isolated DC/DC converter for low side driver.
Bootstrap supply for high-side driver.
Heat sink mounted on the back side of the PCB.
Power connector pin for Vbus, GND and Lx.
Header pin for 12V DC input and PWM inputs.
4 layers FR4 board design.
Board size of 2.6’’x1.7’’x1.25’’ including heat sink.

## Slide 3: Half-Bridge GaN EVB – GaN Daughter Card Details
Tagore GaN
TP44100NM
Power Pins
PCB Edge connector
(Bias Supply and
PWM Pins)
Decoupling
Capacitors
(Ceramic)
P_GND
VBUS
LX
LV side to HV side
Isolation boundary
12V – 12V Isolated DC-DC converter
LV Side
HV Side
HS GaN
LS GaN
Isolated gate drivers

## Slide 4: Half-Bridge GaN EVB – GaN Daughter Card Details
Heatsink
Rear side
Front side

## Slide 5: Tagore GaN HB EVB – Example Use Cases

## Slide 6: Tagore GaN HB EVB – How to Use ? (Mother Board Introduction)
The GaN HB can be tested stand alone. However, it is recommended
to use a dedicated mother board to test the HB EVB. The HB daughter
card can be directly plugged into the mother board, which interfaces
between all the HV/LV input and output voltages/currents.
The block diagram representation of the mother board and the
Daughter card is shown here.
Dead time generation
+12V Input
PWM_HS_IN
PWM_H
PWM_L
+12V Vcc
+5V Output for external circuits (if any)
LDO
+12V supply for Fan
Logic inverter
HB GaN Daughter Card
VBUS
LX
PGND
Vdc_Out
VBUS
PGND
LX
Vdc_Out
GND
CHV
CLV
LV Bias supply and PWM input
Mother board
Power circuit Interface (HV)
The mother board receives a single PWM input (for HS GaN).
The PWM pulses for LS GaN, and the dead time (adjustable) between
the HS and LS GaN’s are generated in the mother board.

## Slide 7: Half-Bridge GaN EVB – Mother Board Details.
Power circuit Interface (HV) cables
(HS PWM)
(LS)
+5V/0V

## Slide 8: Half-Bridge GaN EVB – Mother Board Details.
Bottom side
Top side
5V Linear Regulator IC
Nand Gate IC for complementary PWM, and Dead time generation
HV MLCCs

## Slide 9: Complete Tagore’s HB GaN EVB – Daughter Card Plugged into Mother Board

## Slide 10: Complete Tagore’s HB GaN EVB – Daughter Card Plugged into Mother Board

## Slide 11
Half-Bridge GaN EVB – Daughter Card Schematic

## Slide 12
Half-Bridge GaN EVB – Mother Board Schematic

## Slide 13: Half-Bridge GaN EVB Application – DC-DC Buck Converter
HV Input
(400V Max)
LV Output
(350V Max)
HV Input
(400V Max)
LV Output
(350V Max)
This slide shows an example case, where the EVB can be configured to realize a DC-DC Buck Converter.
The HS GaN acts as the main converter switch, while the LS GaN acts as the synch. Rectifier.
The mother board is used with single PWM input (for HS GaN). The PWM signal for the LS GaN, and the associated dead time (between HS and LS GaN gating pulses) are generated in the Mother board. The dead time can be adjusted by changing two timing resistors. Currently it is set at around 75ns.

## Slide 14
Half-Bridge GaN EVB Application – DC-DC Buck Converter
(HS PWM)
(LS)
(> 750uH)

## Slide 15
Half-Bridge GaN EVB – Buck Converter Switch Waveform
380Vdc
190Vdc
500W
200uH
Fsw: 100kHz
Dead time: 75ns
LX
2A/div
200V/div
Turn on instant of HS GaN
Turn off instant of HS GaN
Typical switching instant voltage and inductor current waveforms

## Slide 16
Half-Bridge GaN EVB – Standard Operation Procedure
Arrange for, a 400V DC source, 500W load resistor, 12V bias supply, 750uH, 4A Inductor, PWM signal source with variable duty cycle and
a cooling fan.
Make the electrical connection as shown in slide 14 (DC-DC buck converter). Keep the 400V DC supply output to 0V and OFF.
Connect the PWM signal generator output to the SMA connector. Set the duty cycle to 48%.
Plug in the daughter card as shown in slides 9 and 10.
Fix two thermocouple probes to the HS and LS GaN to continuously monitor the case temperatures.
Turn on the cooling fan to cool the heat sink fitted on the daughter card.
Gradually increase the HV DC power supply from 0V to 380V, while monitoring the GaN temperatures.
Do the various measurements/probing.
Turn off the HV power supply, if any GaN case temperature exceeds 100 Deg. C open .
The HS and LS GaN dead time is set for 150ns. It can be changed by adjusting the resistors R4 and R5 in the mother board.

## Slide 17: Thank You!